《Diecutting Machine BD-1050C》

》Diecutting Machine BD-1050C >> Machinery Dimension

》Diecutting Machine BD-1050C >> Main Functions

LCD serene dialogue window displays all kinds of information with recording and setting functions. Feeder can start to feed the first sheet of paper during high speed operation with fast speed and high accuracy. Adopts paper catch pincer that can ensure accuracy during high speed operation. Electronic control for slight left and right adjustment of feeder platform. Paper feed belt buffer structure. Thin paper can be die cut easily, quickly, and accurately. Lubrication oil constant temperature control that can solve the unevenness of cold shrinkage and heat expansion problem and can also protect machine from wear and tear. Electronic control digital display for die cut pressure. Operation is easy, clear and fast. Imported excellent hardness die cut steel plate. Solid and durable and is hard to be damaged. Die cut pressure protection device. Automatic shutdown when pressure is over 300 tons so as to ensure mechanical safety. Electronic control air pressure type for wedging of die frame. Speedy, light and easy operation. European main chain and vacuum pump. Durable and not easy to be damaged. Comes with non-stop feeding and delivery with automatic subsidiary paper collection rack. Speedy automatic conversion.

| 》Diecutting Machine BD-1050C >> Machinery Specifications |
| --- |
| max. paper size | 1050mm × 750mm |
| min. paper size | 400mm × 370mm |
| max. die cutting size | 1040mm × 730mm |
| max. cutting pressure | 300tons |
| min./max/ thickness paper | 80g/㎡ ~ 1500g/㎡ |
| max/ corrugated board | 4mm |
| min. gipper margin | 8mm |
| max. machine speed | 7500 Sheets/hr |
| inner size of chase | 1145mm |
| size of steel plate | 1080mm × 736mm |
| max.feeder overlap height （with platform） | 1250mm |
| max. delivery overlap height （with platform） | 1150mm |
| machine total power | 22kw |
| machine length | 6110mm |
| machine width | 3470mm |
| machine heihth | 2500mm |
| total weight(approx.) | 14.3 tons |
| ★ Specifications are change without notice for improvement. |

》Diecutting Machine BD-1050C >> Machinery Introduction

Touch-screen

Display all information during operation. Setting function for die cutting pressure/paper insert length indications etc.

Paper feeding divice

Excellent and delicate feeder design that allows steady and accurate paper feeding Height and angle of one suction and two suctions can be adjusted individually Height and angle of first suction and second suctions can be adjusted individually. Outfitted with preparation paper accumulation platform to enhance production volume and performance. Outfitted with non-stop feeding speedy automatic conversion between main/ auxiliary paper rack.

Conveyance positioning structure

Push/pull device for horizontal positioning.Conversion is easy and simple and facilitate sselection of paper. During operation the two sets or front positioning can arbitrarily adjust the tolerance of front and back/slanting. Double sheet device that can check whether there is double sheet feeding and it will shutdown to protect machine. Automatic shutdown device that can check for abnormal precision of paper feed front / horizontal positioning. Paper feed belt buffer device – to stabilize accuracy of thin paper.

Pressing unit

US import pressure controller.Automatic shutdown when die cut pressure is over 300 tons in order to ensure mechanical safety. Electrical equipment digital control for die cut pressure adjustment.Can be displayed on the screen for recording and setting. Die frame adopts air pressure pinching.

Die cutting unit

Curve operation structure with heavy loading durability Stable pressure, high precision,wear and tear durability. Safety die cutting frame design, Easy installation and dismantling. Rotation die frame design that allows easy replacement of die cutters. Imported excellent hardness die cut steel sheet,durable and wear and tear resistance.

Delivery unit

Brush and lower/ side nozzle are utilized to stabilize effect of uniform paper collection. No-stop delivery for full paper during operation. To set up paper indicator insert device Can set total paper number and automatic shutdown function

寶德企業股份有限公司 　　Baoder　Enterprise　Co.,Ltd.

NO.178-7,Wen-cheng Rd. Taishan,Taishan,Taipei County,Taiwan

TEL：886-2-2900-5551~53　FAX：886-2-2900-8633