《Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF 》

》Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF >> Machinery Dimension

‧

| 》Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF >> Machinery Introduction |
| --- |
| heating plate system |
|  | Hot stamping mould could easily adjust position any time. heat-resistant material and not easy deformation. |
| computerized foil pulling system |
|  | Pulling type of foil set Install the foil is convenient. High precision deliver foil. 2000m foil turntable set. |
| foil heater zone location map hot foil control system |
|  | Hot stamping control system. To set up the hot stamping fuction. Hot stamping heat control system. Accurate heating control. |
| foil rewinding device |
|  | Waste foil in roll doesn’t take speace. No need to use paper core to rewind waste foil. Shaft type and easy to take off. |
| hologram foil stamp system |
|  | Adjustment is convenient. Micro adjust on the computer. High precise hot stamping. You could do three hologram picture together. |
| Foil check/test structure |
|  | To check 12pcs of foils are error or not. To check if the foil is not in position. To see if the foil is broken. Adjust the foil displacement anytime. |
| output foil institution |
|  | output foil institution can push to other side of the machine and be convenient to internal operation. |

| 》Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF >> Machinery Introduction |
| --- |
| touch screen monitor system |
|  | Display all information during operation. Setting function for die cutting pressure/paper insert length indications etc. |
| feeder unit |
|  | Excellent and delicate feeder design that allows stable paper feeding. Preparation paper platform to enhance production and performance. Non-stop feeding The main platform could move left and right. |
| Conveyance positioning structure |
|  | Push/Pull device for horizontal positioning. Front/back positioning adjustment during operation. Double sheet device. |
| die-cutting station |
|  | Safety die cutting frame design, Easy installation and dismantling. Rotation die frame. -design that allows easy replacement of die cutters. Imported excellent hardness die cut steel sheet,durable and wear and tear resistance. |

》Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF >> Main Functions

Computerized foil pulling system with 2 pulls to precisely control the foil length as desired. 12 zone heating unit with precise temperature controller. Heating zones temperature can be set individually. Automatic impression on/off system, with tonnage searching program preset at low tonnage to avoid damaging and reduce the consumption of the paper & foil. Steel plate and mold frame can be close and loose automatically, and easy to operate. LCD screen master all the function, display unusual spot and location, help fasten the diagnosis. Adopts paper catch pincer that can ensure accuracy during high speed operation. Lubrication cooler system avoid high oil temperature, protect machine parts wear and tear. Operate cutting pressure by computer, digital display accurate and speedy. Push and pull 2-in-1 side guide device ease conversion use. Feeding and delivery section attached non-stop device. Speedy & automatic conversion. Feeding belt buffer structure with accurate performance to the thin paper. Hologram system is precision and convenient. The stripping unit is facility and fast. The Foil rewinding device is easy to handle the waste foil. The chain is adopted European brand. Imported excellent hardness die cut steel plate. Solid and durable and is hard to be damaged.

| 》Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF >> Machinery Specifications |
| --- |
| Thickness of the gilt paper | 120g/㎡ ~ 2000g/㎡ |
| foil pulling shafts （optional） | 3 shafts (6 shafts) |
| max. foil diameter | 200mm |
| max. rewind diameter | 250mm |
| foil width | 25mm ~ 1020mm |
| maximum.thickness foil plate | 7mm |
| adjustable temperature | 50℃ ～ 180℃ |
| max.hologram stamping area | 1020mm × 730mm |
| paper front fringe & foil membrane gap | 14mm × 23mm |
| heating zone | 12 |
| max.foil stampspeed | 6000 s/h |
| max.hologram stampong speed | 5000 s/h |
| honeycmb | 1 pes |
| foil stamp power required | 24kw |
| rewind shafts （optional） | 6 shafts (12 shafts) |
| Hologram register unit | 3 shafts |
| Stripping unit | 1 unit |
| ★ Specifications are change without notice for improvement. |

| Automatic Foil Stamping With Embossing And Diecutting Platen BD-1050CSF >> Die Cutting Specifications |
| --- |
| max. paper size | 1050mm × 750mm |
| min. paper size | 400mm × 370mm |
| max. die cutting size | 1040mm × 730mm |
| max. cutting pressure | 300tons |
| min./max. thickness paper | 80g/㎡ ~ 1500g/㎡ |
| max. corrugated board | 4mm |
| min. gripper margin | 8mm |
| max. machine speed | 7500 Sheets/hr |
| inner size of chase | 1145mm × 755mm |
| size of steel plate | 1080mm × 736mm |
| max. feeder overlap height （with platform〉 | 1250mm |
| max. delivery overlap height（with platform） | 1150mm |
| machine total power | 20kw |
| machine length | 7060mm |
| machine width | 2750mm |
| machine height | 5164mm |
| machine weight〈approx.〉 | 18 tons |

寶德企業股份有限公司 　　Baoder　Enterprise　Co.,Ltd.

NO.178-7,Wen-cheng Rd. Taishan,Taishan,Taipei County,Taiwan

TEL：886-2-2900-5551~53　FAX：886-2-2900-8633